INVESTIGATION OF PERIODIC TEST POLICY FOR STANDBY UNIT IN PRIORITY STANDBY REDUNDANT SYSTEM

## J.P. Moon1), Y.B. Kim2), J.H. Park3) and C.H. Lie4)

1)Seoul National University, Korea (chl@cybernet.snu.ac.kr)

2)Seoul National University, Korea (chl@cybernet.snu.ac.kr)

3)Seoul National University, Korea (chl@cybernet.snu.ac.kr)

4)Seoul National University, Korea (chl@cybernet.snu.ac.kr)

### Abstract

## We analyze the availability of the standby unit and Mean Time To Failure(MTTF) of the priority statndby redundant system to determine an appropriate periodic test interval for standby unit. Firstly, we derive the limiting availability for the standby unit by considering three failure types. These are failures during standby period(type I failure), test-induced failures at the start of the test(type II failure) and operating failures during the test period due to the aging effect (type III failure). Secondly, we derive MTTF for 1-out-of-2:G priority standby redundant system. Availability for the standby unit and modified regenerative technique are utilized in constructing the integral equations that represent transitions between system states. By taking Laplace transformations for the integral equations, the transformed form of the probability density function of the system is derived from which MTTF of the system is finally obtained. To identify relationships between the optimal periodic test interval and various failure characteristics of the standby unit, several experiments are performed assuming Weibull distribution as an operating time distribution of the standby unit. The result of this paper can be applied to determine an appropriate test interval for the standby unit in priority standby redundant system to ensure higher reliability characteristics.

Keywords : Priority Standby Redundant System, Periodic Test, MTTF, Availability, Laplace Transformation

1.	INTRODUCTION

A priority-standby redundant structure is considered, which consists of an operating unit and a standby unit. The standby unit is called in for the operation only when the priority unit is failed and being repaired. An example of such a structure is the cooling system in the nuclear power plant with a diesel generator as a standby unit. Assuming the standby unit can fail during the standby period, the periodic test is considered for the standby unit[1-3, 5-8]. Although the periodic test is capable of detecting failures during the standby period, it can cause test-induced failures for the standby unit at the start of the test[2,4-8]. Also, the aging process of the standby unit during the test period need to be taken into account, which is not treated in the existing studies. Therefore investigation of an appropriate test interval considering such aspects of the standby unit is very important.

Availability of the standby unit in the priority-standby redundant system is so critical to system performance that the unavailability of the standby unit in the priority-standby redundant system would have catastrophic consequences. For example, the failure of a diesel generator when demanded in the nuclear power plant would cause a meltdown of the nuclear reactor. Therefore the availability of the standby unit is considered as a meaningful measure of performance. In viewpoint of the priority-standby redundant system, MTTF is considered to be a meaningful measure of performance because a failure of the system is catastrophic.

In this study, therefore, we adopt the availability of the standby unit as well as MTTF of the priority-standby redundant system as meaningful measures of system performance. Firstly, we derive the limiting availability for the standby unit by incorporating three failure types : (i) type I failure ; failures during standby period, (ii) type II failure ; test-induced failures at the start of the test and (iii) type III failure ; operating failures during the test period due to the aging effect. Secondly, we illustrate the derivation procedure of MTTF for 1-out-of-2:G priority standby system. Using these measures, an appropriate test interval for the standby unit in 1-out-of-2:G priority-standby redundant system is investigated.

# Notations & Nomenclature

test interval[test period] for the standby unit

probability of type II failure

operating[repair] time distribution of the standby unit

limiting availability of the standby unit

standby failure [overhaul] time distribution of the standby unit

probability of type I failure in each test interval

operating[repair] time distribution of the priority unit

system state vector ; x[y] represents the state of priority unit[standby unit]

,

system reliability function [probability density function] given the system’s initial state is (x, y)

system reliability function given the system’s initial state is (r, o) and standby unit’s age is (i.e.,  is the cumulative test time before the standby unit is called in for the operation in place of the priority unit)

Laplace transform of

# Assumptions

1. Three failure types of the standby unit are independent of each other.

2. Both type I failure rate and probability of type II failure are constants.

3. Type III failure rate is increasing over cumulative test time until the standby unit is called in for the operation in place of the priority unit, i.e.,

4. Standby unit is overhauled after each mission (operation in place of the priority unit) and is restored to the state of as-good-as-new

5. Demand for the standby unit occurs according to the Homogeneous Poisson Process

6. Repair time distributions of standby unit and priority unit are respectively arbitrary.

# 2. 	LIMITING AVAILABILITY OF STANDBY UNIT

To derive availability of the standby unit, mean cycle time and mean up time must be calculated respectively. The standby unit undergoes standby and test states repeatedly until a failure for the standby unit occurs. The failure rate of the standby unit is constant during standby period. The failure rate function of the standby unit during test period is increasing function of the cumulative test duration. If no failure is found during a specific test period, the state of the standby unit at the beginning of the next test period is equal to that at the end of the previous test period. If any failure is found through the test, the standby unit undergoes repair action and is restored to the state of as-good-as-new. Therefore, from the initial standby status to the completion of the repair of the standby unit constitutes a cycle. Fig.1 illustrates such aspects of the failure rate function of the standby unit.

Fig. 1  Failure rate function of standby unit

Fig. 2-1 ~ Fig. 2-3 represent the mean cycle time and the mean up time for the following three failure types of the standby unit :

(i) type I failure ; failure during standby period,

(ii) type II failure ; test-induced failure at the start of the test,

(iii) type III failure ; operating failure during the test period

2.1	Mean Cycle Time(MCT)

To derive MCT of the standby unit, three failure types of the standby unit should be considerd.

Firstly, if standby unit fails according to the failure type I, i.e., the standby unit has failed during the standby period and this failure is found at the beginning of the test as depicted in Fig. 2-1, the mean cycle time due to failure type I can be written as

.     		(1)

Fig. 2-1 Mean cycle time of type I failure case

Secondly, if standby unit fails according to the failure type II(test-induced failure case), i.e., the standby unit fails and founded at the start of the test as depicted in Fig. 2-2, the mean cycle time due to failure type II can be written as

,  	(2)

Fig. 2-2 Mean cycle time of type II failure case

Lastly, if standby unit fails according to the failure type III, i.e., the standby unit fails during the test operation and the failure is founded immediately as depicted in Fig. 2-3, the mean cycle time due to failure type III can be written as

.     			(3)

Fig. 2-3 Mean cycle time of type III failure case

Therefore, the mean cycle time can be written as

.        			(4)

2.2 	Mean Up Time(MUT)

In a similar way, the mean up time(MUT) of the standby unit during cycle is derived by considering three failure types. The MUT due to three failure types as depicted in Fig. 2-1 ~ Fig. 2-3 can be respectively be written as

,  		(5)

,          		(6)

.   			(7)

Therefore, the mean up time can be written as

.					(8)

By utilizing the renewal theory, limiting availability of the standby unit during the standby period can be derived as

.			         					(9)

3. 	MTTF FOR 1-OUT-OF-2:G PRIORITY STANDBY REDUNDANTSYSTEM

Considering both states of a priority unit and a standby unit, the operating mechanism of 1-out-of-2:G priority standby redundant system can be represented by Fig. 3.

Fig. 3 Operating mechanism of 1-out-of-2:G priority standby redundant system

We assume failure times of the priority unit are exponentially distributed(i.e., demand for the standby unit follows Homogeneous Poisson Process). We also assume the standby unit is overhauled after each mission (operation in place of the priority unit) and restored to the state of as-good-as-new. By identifying pairs of the states of the standby unit and the priority unit, integral equations are constructed, which represent transitions between pairs of states. An availability for the standby unit and modified regenerative technique are utilized in constructing the integral equations. As a result, the following integral equations are obtained.[5]

(10)

(11)

(12)

Equation (10) represents the system reliability function given the state of the system is

Equation (10) is composed of two terms. The first term is the survival probability of the priority unit up to time  and the second term is survival probability of the system during  given the state of the system is  on the condition that the priority unit has failed at time  and the state of the standby unit is good at time .

In constructing equation (10) and (11), the fact that the transition time from the state  to  neighbor states is dependent on the standby unit’s age(previous operation time) must be considered. If  can be obtained in a closed form, MTTF can be calculated easily. , however, cannot be obtained in a closed form. Therefore, we utilize Laplace transform of , , to calculate system MTTF and finally MTTF of the priority standby redundant system can be calculated using equation (13) [5].

(13)

#### 4. 	NUMERICAL EXAMPLE

To identify relationships between the optimal periodic test interval and various failure characteristics of the standby unit, several experiments are performed using the availability of the standby unit and MTTF of the priority standby redundant system as measures of system performances.

In the experiments, life distribution of the standby unit in test operation is assumed to be Weibull with scale and shape parameters of 1 and 2 respectively. Repair time distributions of standby unit and priority unit are assumed to be the exponential with parameters of 1 and 0.5 respectively. Probability of type II failure,  is fixed at 0.2.

Variations of the optimal periodic test interval are observed with respect to the changes of type I failure rate for fixed . These variations are illustrated in Fig. 4 and Fig. 5 using availability and MTTF as respective measures of system performances. Results show that the optimal interval increases as type I failure rate decreases.

Fig. 4 Availability versus and T( and )

Fig. 5 MTTF versus T(,  and )

Variations of the optimal test interval with respect to the changes of test duration time (aging effect during test period) are observed for fixed . Results are depicted in Fig. 6 and Fig. 7 against respective performance measures of availability and MTTF. Optimal test interval is shown to be increased as the test duration time  increases (as the aging effect increases).

Fig. 6  Availability versus and T( and )

Fig. 7 MTTF versus T(,  and )

5.	CONCLUSIONS

We analyze the availability of the standby unit and Mean Time To Failure(MTTF) of the priority standby redundant system to determine an appropriate periodic test interval for the standby unit. Especially, we consider operating failures due to the aging effect during the test period, which is not treated in the previous works. By establishing integral equations and deriving the Laplace transform of the system probability density function, we can obtain system MTTF. Results of the experiments show that the optimal periodic test interval increases as type I failure rate decreases. Also, the optimal periodic test interval is shown to be increased as the aging effect of the standby unit increases. These results agree with what we have expected. An appropriate periodic test interval for the standby unit, however, can reasonably be identified under three types of failures of standby unit. Although three failure types of the standby unit are treated as independent in this study, the degree of dependency between three failure types need to be investigated further, which is left as future research works.

### 6.	Acknowledgment

This research has been partially supported by the Brain Korea 21 Project as well as by the KOSEF project (project No. : 971-1012-068-2).

### References

1)	C.G. Chou, D.A. Butler, “Assessment of Hazardous-Inspection Policies”, Naval Research Logistics Quarterly, Vol. 30, 1983, pp171-177.

2)	Valdez-Flores, R. M. Feldman, "A Survey of Preventive Maintenance Models for Stochastically Deteriorating Single-Unit Systems", Naval Research Logistics Quarterly, Vol. 36, 1989, pp.419-446.

3)	D.A. Butler, "A Hazardous-Inspection Policies", Management Sciences, Vol. 25, No. 1, 1979, pp79-89.

4)		I.S. Kim, S.A. Martorell, W. E. Vesely and P. K. Samanta, "Risk analysis of surveillance requirements including their adverse effects", Rel. Eng. and System Safety, Vol. 45, 1994, pp.225-234.

##### 5)		J.P. Moon, C.H. Lie, “Reliability Analysis of Priority-Standby Redundant System under Periodic Tests for Standby Unit”, working paper, Dep. of Industrial Engineering, Seoul National University, 2000.

6)		J.K. Vaurio, "Optimization of test and maintenance intervals based on risk and cost", Rel. Eng. and System Safety, Vol. 49, 1995, pp.23-36.

7)		S. H. Sim, "Unavailability Analysis of Periodically Tested Components of Dormant Systems", IEEE Trans. on Rel., Vol. R-34, No. 1, 1985, pp.88-91.

8)		S. H. Sim, "Reliability of Standby Equipment with Periodic Testing", IEEE Trans. on Rel., Vol. R-36, No. 1, 1987, pp.117-123.